## Slide 1: Theory of Elasticity
Introduction
Concerned with determining stress, strain, and displacement distribution in an elastic solid under the inﬂuence of external forces
Using continuum mechanics, formulation establishes a mathematical boundary value problem model – set of governing partial differential field equations with particular boundary conditions
Engineering Applications
Aeronautical/Aerospace Engineering - stress, fracture, and fatigue analysis in aero structures.
Civil Engineering - stress and deﬂection analysis of structures including rods, beams, plates, and shells; geomechanics involving the stresses in soil, rock, concrete, and asphalt materials.
Materials Engineering - to determine the stress ﬁelds in crystalline solids, around dislocations and in materials with microstructure.
Mechanical Engineering - analysis and design of machine elements, general stress analysis, contact stresses, thermal stress analysis, fracture mechanics, and fatigue.
Subject also provides basis for advanced studies in inelastic material behavior including plasticity and viscoelasticity, and to computational stress analysis using ﬁnite/boundary element methods.
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 2: Basic Methods of Stress & Deflection Analysis
Mechanics of Materials (Strength of Materials)
Simplified analysis based upon the use of assumptions related to the geometry of the deformation, e.g., plane sections remain plane. See Appendix D in text for review.
Theory of Elasticity
General approach using principles of continuum mechanics. Develops mathematical boundary-value problems for solution to the stress, strain and displacement distributions in a given body.
Computational Methods: Finite Element, Boundary Element, and Finite Difference
Each method discretizes body under study into many computational elements or cells. Solution is then determined over each element or cell. Computers are used to handle detailed calculations.
Experimental Stress Analysis
Numerous techniques such as photoelasticity, strain gages, brittle coatings, fiber optic sensors, Moire' holography, etc. have been developed to experimentally determine the stress, strain or displacements at specific locations in models or actual structures and machine parts.
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island