## Slide 1: Common Variable Types in Elasticity
Elasticity theory is a mathematical model of material deformation. Using principles of continuum mechanics, it is formulated in terms of many different types of field variables specified at spatial points in the body under study. Some examples include:
Scalars - Single magnitude mass density , temperature T, modulus of elasticity E, . . .
Vectors – Three components in three dimensions displacement vector
Matrices – Nine components in three dimensions
stress matrix
Other – Variables with more than nine components
Chapter 1 Mathematical Preliminaries
, e1, e2, e3 are unit basis vectors
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 2: Index/Tensor Notation
With the wide variety of variables, elasticity formulation makes use of a tensor formalism using index notation. This enables efficient representation of all variables and governing equations using a single standardized method.
Index notation is a shorthand scheme whereby a whole set of numbers or components can be represented by a single symbol with subscripts
In general a symbol aij…k with N distinct indices represents 3N distinct numbers
Addition, subtraction, multiplication and equality of index symbols are defined in the normal fashion; e.g.
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 3: Notation Rules and Definitions
Summation Convention - if a subscript appears twice in the same term, summation over that subscript from one to three is implied; for example
A symbol aij…m…n…k is said to be symmetric with respect to index pair mn if
A symbol aij…m…n…k is said to be antisymmetric with respect to index pair mn if
Useful Identity
. . . symmetric
. . . antisymmetric
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 4
The matrix aij and vector bi are specified by
Determine the following quantities:
Indicate whether they are a scalar, vector or matrix.
Following the standard definitions given in section 1.2,
Example 1-1: Index Notation Examples
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 5: Special Index Symbols
Kronecker Delta
Properties:
Alternating or Permutation Symbol
123 = 231 = 312 = 1, 321 = 132 = 213 = -1, 112 = 131 = 222 = . . . = 0
Useful in evaluating determinants
and vector cross-products
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 6: Coordinate Transformations
v
e1
e3
e2
e3
e2
e1
x3
x1
x2
x1
x2
x3
To express elasticity variables in different coordinate systems requires development of transformation rules for scalar, vector, matrix and higher order variables – a concept connected with basic definitions of tensor variables. The two Cartesian frames (x1,x2,x3) and differ only by orientation
Using Rotation Matrix
transformation laws for Cartesian vector components
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 7: Cartesian Tensors General Transformation Laws
Scalars, vectors, matrices, and higher order quantities can be represented by an index notational scheme, and thus all quantities may then be referred to as tensors of different orders. The transformation properties of a vector can be used to establish the general transformation properties of these tensors. Restricting the transformations to those only between Cartesian coordinate systems, the general set of transformation relations for various orders are:
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 8
Example 1-2 Transformation Examples
The components of a first and second order tensor in a particular coordinate frame are given by
Determine the components of each tensor in a new coordinate system found through a rotation of 60o (/6 radians) about the x3-axis. Choose a counterclockwise rotation when viewing down the negative x3-axis, see Figure 1-2.
The original and primed coordinate systems are shown in Figure 1-2. The solution starts by determining the rotation matrix for this case
The transformation for the vector quantity follows from equation (1.5.1)2
and the second order tensor (matrix) transforms according to (1.5.1)3
x3
x1
x2
x1
x2
x3
60o
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 9: Principal Values and Directions for Symmetric Second Order Tensors
The direction determined by unit vector n is said to be a principal direction or eigenvector of the symmetric second order tensor aij if there exists a parameter  (principal value or eigenvalue) such that
Relation is a homogeneous system of three linear algebraic equations in the unknowns n1, n2, n3. The system possesses nontrivial solution if and only if determinant of coefficient matrix vanishes
scalars Ia, IIa and IIIa are called the fundamental invariants of the tensor aij
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 10: Principal Axes of Second Order Tensors
It is always possible to identify a right-handed Cartesian coordinate system such that each axes lie along principal directions of any given symmetric second order tensor. Such axes are called the principal axes of the tensor, and the basis vectors are the principal directions {n(1), n(2) , n(3)}
x3
x1
x2
Principal Axes
Original Given Axes
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 11
Example 1-3 Principal Value Problem
Determine the invariants, and principal values and directions of
First determine the principal invariants
The characteristic equation then becomes
Thus for this case all principal values are distinct
For the 1 = 5 root, equation (1.6.1) gives the system
which gives a normalized solution
In similar fashion the other two principal directions are found to be
It is easily verified that these directions are mutually orthogonal.
Note for this case, the transformation matrix Qij defined by (1.4.1) becomes
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 12: Vector, Matrix and Tensor Algebra
Scalar or Dot Product
Vector or Cross Product
Common Matrix Products
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 13: Calculus of Cartesian Tensors
Field concept for tensor components
Comma notation for partial differentiation
If differentiation index is distinct, order of the tensor will be increased by one; e.g. derivative operation on a vector produces a second order tensor or matrix
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 14: Vector Differential Operations
Directional Derivative of Scalar Field
Common Differential Operations
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 15: Example 1-4: Scalar/Vector Field Example
Scalar and vector field functions are given by
Calculate the following expressions, , 2,  ∙ u, u,   u.
Using the basic relations:

2
 ∙ u
u
  u
Contours =constant and vector distributions of 
vector field  is orthogonal to -contours (ture in general )
x
y
- (satisfies Laplace equation)
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 16: Vector/Tensor Integral Calculus
Divergence Theorem
Stokes Theorem
Green’s Theorem in the Plane
Zero-Value Theorem
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 17: Orthogonal Curvilinear Coordinate Systems
Cylindrical Coordinate System (r,,z)
Spherical Coordinate System (R,,)
e3
e2
e1
x3
x1
x2
R


Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 18: General Curvilinear Coordinate Systems
Common Differential Forms
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 19: Example 1-5: Polar Coordinates
From relations (1.9.5) or simply using the geometry shown in Figure
The basic vector differential operations then follow to be
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island