## Slide 1: Chapter 5 Formulation and Solution Strategies
Review of Basic Field Equations
Compatibility Relations
Strain-Displacement Relations
Equilibrium Equations
Hooke’s L aw
15 Equations for 15 Unknowns ij , eij , ui
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 2: Boundary Conditions
Mixed Conditions
Symmetry Line
Rigid-Smooth Boundary Condition Allows Specification of Both Traction and Displacement But Only in Orthogonal Directions
R
S
R
Su
St
R
S
u
Traction Conditions
Displacement Conditions
T(n)
x
y
S = St + Su
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 3: Boundary Conditions on Coordinate Surfaces On Coordinate Surfaces the Traction Vector Reduces to Simply Particular Stress Components
(Cartesian Coordinate Boundaries)
(Polar Coordinate Boundaries)

r
r

r
r
r

x
xy
y
x
y
x
xy
y
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 4: Boundary Conditions on General Surfaces On General Non-Coordinate Surfaces, Traction Vector Will Not Reduce to Individual Stress Components and General Traction Vector Form Must Be Used
Two-Dimensional Example
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 5: Example Boundary Conditions
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 6: Interface Boundary Conditions
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 7: Fundamental Problem Classifications
Problem 1 (Traction Problem) Determine the distribution of displacements, strains and stresses in the interior of an elastic body in equilibrium when body forces are given and the distribution of the tractions are prescribed over the surface of the body,
Problem 2 (Displacement Problem) Determine the distribution of displacements, strains and stresses in the interior of an elastic body in equilibrium when body forces are given and the distribution of the displacements are prescribed over the surface of the body.
Problem 3 (Mixed Problem) Determine the distribution of displacements, strains and stresses in the interior of an elastic body in equilibrium when body forces are given and the distribution of the tractions are prescribed as per (5.2.1) over the surface St and the distribution of the displacements are prescribed as per (5.2.2) over the surface Su of the body (see Figure 5.1).
R
S
T(n)
R
S
u
R
Su
St
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 8: Stress Formulation Eliminate Displacements and Strains from Fundamental Field Equation Set (Zero Body Force Case)
Equilibrium Equations
Compatibility in Terms of Stress: Beltrami-Michell Compatibility Equations
6 Equations for 6 Unknown Stresses
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 9: Displacement Formulation Eliminate Stresses and Strains from Fundamental Field Equation Set (Zero Body Force Case)
Equilibrium Equations in Terms of Displacements: Navier’s/Lame’s Equations
3 Equations for 3 Unknown Displacements
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 10: Summary of Reduction of Fundamental Elasticity Field Equation Set
General Field Equation System
(15 Equations, 15 Unknowns:)
Stress Formulation
(6 Equations, 6 Unknowns:)
Displacement Formulation
(3 Equations, 3 Unknowns: ui)
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 11: Principle of Superposition
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 12: Saint-Venant’s Principle
The stress, strain and displacement fields due to two different statically equivalent force distributions on parts of the body far away from the loading points are approximately the same
Stresses approximately the same
Boundary loading T(n) would produce detailed and characteristic effects only in vicinity of S*. Away from S* stresses would generally depend more on resultant FR of tractions rather than on exact distribution
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 13: General Solution Strategies Used to Solve Elasticity Field Equations
Direct Method - Solution of field equations by direct integration. Boundary conditions are satisfied exactly. Method normally encounters significant mathematical difficulties thus limiting its application to problems with simple geometry.
Inverse Method - Displacements or stresses are selected that satisfy field equations. A search is then conducted to identify a specific problem that would be solved by this solution field. This amounts to determine appropriate problem geometry, boundary conditions and body forces that would enable the solution to satisfy all conditions on the problem. It is sometimes difficult to construct solutions to a specific problem of practical interest.
Semi-Inverse Method - Part of displacement and/or stress field is specified, while the other remaining portion is determined by the fundamental field equations (normally using direct integration) and boundary conditions. Constructing appropriate displacement and/or stress solution fields can often be guided by approximate strength of materials theory. Usefulness of this approach is greatly enhanced by employing Saint-Venant’s principle, whereby a complicated boundary condition can be replaced by a simpler statically equivalent distribution.
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island

## Slide 14: Mathematical Techniques Used to Solve Elasticity Field Equations
Analytical Solution Procedures
- Power Series Method
- Fourier Method
- Integral Transform Method
- Complex Variable Method
Approximate Solution Procedures
- Ritz Method
Numerical Solution Procedures
- Finite Difference Method (FDM)
- Finite Element Method (FEM)
- Boundary Element Method (BEM)
Elasticity Theory, Applications and Numerics M.H. Sadd , University of Rhode Island